CMG-6TD CALIBRATION

| WORKS ORDER: | 2591 | DATE: | 22 October 2004 |
| --- | --- | --- | --- |
| SERIAL NUMBER: | T6294 | TESTED BY: | ENS |

|  |  | Velocity | Digitiser | Digital |
| --- | --- | --- | --- | --- |
|  |  | Response | Output | Output |
|  |  | V/m/s | uV/count | m/s/count |
| VERTICAL |  | 1039.49 | 0.2575 | 2.477E-10 |
| NORTH/SOUTH |  | 1104.32 | 0.2594 | 2.349E-10 |
| EAST/WEST |  | 1259.73 | 0.2544 | 2.019E-10 |
|  |  | Mass Position | Mass Position | Mass Position |
|  | Coil Constant | Response | Digital Output | Digital Output |
|  | A/m/s2 | V/m/s2 | uV/count | m/s2/count |
| VERTICAL | 0.0026 | 7.80 | 0.5846 | 7.498E-08 |
| NORTH/SOUTH | 0.0028 | 8.28 | 0.5832 | 7.041E-08 |
| EAST/WEST | 0.0031 | 9.45 | 0.5845 | 6.187E-08 |
| Current Consumption: @12V ( ±10 mA) | 79mA |
| This sensor operates from 10 to 36 Volts only. |  |

POLES AND ZERO TABLE

WORKS ORDER NUMBER:	2591

SENSOR SERIAL NO:  		T6294

Velocity response output:

| POLES (HZ) | ZEROS HZ |
| --- | --- |
| -23.65e-3 + 23.65e-3j | -5.03207 |
| -23.65e-3 - 23.65e-3j | 0 |
| -393.011 | 0 |
| -7.4904 |  |
| -53.5979 - 21.7494j |  |
| -53.5979 + 21.7494j |  |
| Normalizing factor at 1 Hz: A =1.983*10^6 |  |

Sensor Sensitivity:		See Calibration Sheet.

NOTE:  The above poles and zeros apply to the vertical and the horizontal sensors and are given in units of Hz.  To convert to Radian/sec multiply each pole or zero with 2  The normalizing factor A should also be recalculated.